## Slide 1: System Components

## Slide 2: What is a System?
In system administration, the word system is used to refer both to the operating system of a computer and often, collectively the set of all computers that cooperate in a network. If we look at computer systems analytically, we would speak more precisely about human–computer systems:

## Slide 3: (human–computer system).
An organized collaboration between humans and computers to solve a problem or provide a service. Although computers are deterministic, humans are non-deterministic, so human–computer systems are non-deterministic.

## Slide 4: Operating system
The term operating system has no rigorously accepted definition. Today, it is often thought of as the collection of all programs bundled with a computer, combining both in a kernel of basic services and utilities for users;

## Slide 5: Network infrastructure
There are three main components in a human–computer system
• Humans: who use and run the fixed infrastructure, and cause most problems.
• Host computers: computer devices that run software. These might be in a fixed location, or mobile devices.
• Network hardware: This covers a variety of specialized devices including the following key components:

## Slide 6: Cont…
dedicated computing devices that direct traffic around the Internet. Routers talk at the IP address level, or ‘layer 3’,1 simplistically speaking.
– Switches: fixed hardware devices that direct traffic around local area networks. Switches talk at the level of Ethernet or ‘layer 2’ protocols,
– Cables: There are many types of cable that interconnect devices: fiberoptic cables, twisted pair cables, etc.

## Slide 7: Cont…

## Slide 8: Computer

## Slide 9: Cont…
All contemporary computers in common use are based on the Eckert–Mauchly–von Neumann architecture [235], sketched in figure 2.2. Each computer has a clock which drives a central processor unit (CPU), a random access memory (RAM) and an array of other devices, such as disk drives. In order to make these parts work together, the CPU is designed to run programs which can read and write to hardware devices. The most important program is the operating system kernel. On top of this are software layers that provide working abstractions for programmers and users. These consist of files, processes and services. Part of ‘the system’ refers to the network devices that carry messages from computer to computer, including the cables themselves. Finally, the system refers to all of these parts and levels working together.

## Slide 10: Handling hardware
To be a system administrator it is important to have a basic appreciation of the frailties and procedures surrounding hardware. In our increasingly virtual world of films and computer simulations, basic common-sense facts about the laws of physics are becoming less and less familiar to us, and people treat fragile equipment with an almost casual disregard.

## Slide 11
Today we are far too blasé towards electronic equipment.
Never insert or remove power cords from equipment without ensuring that it is switched off.
Take care when inserting multi-pin connectors that the pins are oriented the right way up and that no pins are bent on insertion.

## Slide 12: Cont….
Read instructions: When dealing with hardware, one should always look for and read instructions in a manual. It is foolish to make assumptions about expensive purchases. Instructions are there for a reason.
Interfaces and connectors: Hardware is often connected to an interface by a cable or connector. Obtaining the correct cable is of vital importance. Many manufacturers use cables which look similar, superficially, but which actually are different. An incorrect cable can result in damage to an interface. Modem cables in particular can damage a computer or modem if they are incorrectly wired, since some computers supply power through these cables which can damage equipment that does not expect to find a power supply coming across the cable.

## Slide 13: Handling components:
Modern day CMOS chips work at low voltages (typically 5 volts or lower). Standing on the floor with insulating shoes, you can pick up a static electric charge of several thousand volts. Before touching any computer components, earth yourself by touching the metal casing of the computer. If you are installing equipment inside a computer, wear a conductive wrist strap. Avoid wearing rubber sandals or shoes that insulate you from Earth when dealing with open-case equipment, since these cause the body to build up charge that can discharge through that equipment; on the other hand it is a good idea to wear rubber soles when working around high voltage or current sources

## Slide 14: Disks
Disk technology has been improving steadily for two decades. The most
common disk types, in the workplace, fall into two families: ATA (formerly IDE) and SCSI. The original IDE (Integrated Drive Electronics) and SCSI (Small Computer Software Interface) had properties that have since evolved faster than the prejudices about them. ATA disks are now generally cheaper than SCSI disks (due to volume sales) and excel at sequential access, but SCSI disks have traditionally been more efficient at handling multiple accesses due to a multitasking bus design, and are therefore better in multitasking systems, where random access is important. However, filesystem design also plays an important role in determining the perceived performance of each; i.e. how operating systems utilize buses during updates is at least as important as bus performance itself.

## Slide 15: Memory
Memory chips are sold on small pluggable boards. They are sold in different sizes and with different speeds. A computer has a number of slots where they can be installed. When buying and installing RAM, remember
– The physical size of memory plugins is important. Not all of them fit into
all sockets.
– Memory is sold in units with different capacities and data rates. One
must find out what size can be used in a system. In many cases one may
not mix different types.
– There are various incompatible kinds of RAM that work in different ways.
Error correcting RAM, for instance, is tolerant to error from external noise
sources like cosmic rays and other ultra short wave disturbances. It is
recommended for important servers, where stability is paramount.
– On some computers one must fill up RAM slots in a particular order,
otherwise the system will not be able to find them.

## Slide 16: Lightning
strikes can destroy fragile equipment. No fuse will protect hardware from a lightning strike. Transistors and CMOS chips burn out much faster than any fuse. Electronic spike protectors can help here, but nothing will protect against a direct strike.
Power: failure can cause disk damage and loss of data. A UPS (uninterruptible power supply) can help.

## Slide 17: Heat
Blazing summer heat or a poorly placed heater can cause systems to overheat and suddenly black out. One should not let the ambient temperature near a computer rise much above 25 degrees Centigrade. Clearly some equipment can tolerate heat better than other equipment. Bear in mind that metals expand significantly, so moving parts like disks will be worst affected by heat. Increased temperature also increases noise levels that can reduce network capacities by a fraction of a percent. While this might not sound like much, a fraction of a percent of a Giga-bit cable is a lot of capacity. Heat can cause RAM to operate unpredictably and disks to misread/miswrite. Good ventilation is essential for computers and screens to avoid electrical faults.

## Slide 18: Cold
Sudden changes from hot to cold are just as bad. They can cause unpredictable changes in electrical properties of chips and cause systems to crash. In the long term, these changes could lead to cracks in the circuit boards and irreparable chip damage.

## Slide 19: Humidity
In times of very cold weather and very dry heat, the humidity falls to very low levels. At these times, the amount of static electricity builds up to quite high levels without dissipating. This can be a risk to electronic circuitry. Humans pick up charge just by walking around, which can destroy fragile circuitry. Paper sticks together causing paper crashes in laser printers. Too much humidity can lead to condensation and short circuits.

## Slide 20: Operating System
An operating system has a number of key elements:
(i) a technical layer of software:
for driving the hardware of the computer, like disk drives, the keyboard and the screen;
(ii) a filesystem: which provides a way of organizing files logically, and
(iii) a simple user interface :
which enables users to run their own programs and to
manipulate their files in a simple way.

## Slide 21: Cont…
Software system or kernel:
Is Of central importance to an operating system is a core which is responsible for allocating and sharing the resources of the system between several running programs or processes. It is supplemented by a number
of supporting services (paging, RPC, FTP, WWW etc.)

## Slide 22
Distributed operating systems:
in which execution of programs and sharing of resources happens without regard for hardware boundaries;
Network operating systems:
in which a central server adds functionality to relatively dumb workstations. Sometimes programs which do not affect the job of sharing resources are called user programs.

## Slide 23: Filesystems
Files and file systems are at the very heart of what system administration is about. Almost every task in host administration or network configuration involves making changes to files. We need to acquire a basic understanding of the principles of file systems, so what better way than to examine some of the most important file systems in use today. Specifically what we are interested in is the user interfaces to common file systems, not the technical details which are rather fickle. We could, for instance, mention the fact that old file systems were only 32 bit addressable and therefore supported a maximum partition size of 2GB or 4GB, depending on their implementation details, or that newer file systems are 64 bit addressable and therefore have essentially no storage limits.